Making Use of Python
David House, David Story, Joe Haun

---
Requirements
- PyCharm Installed
- Serial Library Installed
- Binascii Library Installed

---
Python Concepts
- Import
- Def
- Print

---
Python Concepts
- Serial Class
  - Initialization Parameters

---
Class Functions
- open()
  - Opens the port
- close()
  - Closes the port
- read(n)
  - Reads n bytes of data
- write(data)
  - Sends data through the port

---
Class Functions
- port
  - (string) Set/Get port name value
- baudrate
  - (int) Set/Get baudrate value
- bytesize
  - (int) Set/Get bytesize value
- timeout
  - (float) Set/Get read timeout value

---
Initializing Port
- Two Methods with Identical Results
  - Initializing with constructor and all relevant values
  - Initializing an empty port object and using setters to initialize various values

---
Initializing Port
Method 1
- Using the Setters provided
  - Initialize Blank Serial Object
  - Assign Port Name
    - Note: This name is for Linux/MacOS. For Windows it will be COM3 instead.

---
Initializing Port
Method 1
- Using the Setters provided
  - Set Baudrate
  - Set read timeout value (in seconds)

---
Initializing Port
Method 1
- Using the Setters provided
  - Set the byte size to be sent/received
  - Set the parity (if any) for transmission
    - Note: This will add extra bits sent to help insure data integrity

---
Initializing Port
Method 1
- Using the Setters provided
  - Set the number of stop bits to be sent
- The Port is now setup for transfer of data

---
Initializing Port
Method 2
- Use the Constructor and set all parameters desired at once
- The port is now setup for the transfer of data

---
Hardware Interfacing
- Setup a Python script to interface with provided microcontroller
  - Baudrate – 9600
  - Bytesize – 8
  - Stopbits – 0
  - Parity – None

---
Board Program
Serial String Format
- Enabling Functions
  - First Character is Feature
    - Sending “D” turns on Digital Input
  - Second is the Pin Number
    - Sending “1” sets function on Pin 1
  - Third is the Initial Output
    - Sending “0” sets the pin to output 0 initially

---
Board Program
Challenges
- Send Eight Bytes of Data to another person
  - Using a serial connection
  - Using a parallel connection
- Read in and report an analog signal

---
Board Program
Available Functions
Function	Character	Availability
Digital Output	D
Digital Input	d
Analog Input	a
SPI
UART